## Slide 1
Kansas Geological Survey Activities in Support of Groundwater Conservation Efforts in Wichita County
Kansas Geological Survey
University of Kansas
Wichita County Public Meeting
August 28, 2024

## Slide 2
Kansas Index Well Program
Kansas Geological Survey
Since monitoring began, end-of-season recovery is similar regardless of past pumping or climatic conditions

## Slide 3
Index Wells Recovery Curves, Scott County
Kansas Geological Survey
Water level change starting at the end-of-season pumping (September to April~June)
Recovery is similar each year
“Net Inflow”
  Everything flowing in and out of the aquifer except pumping

## Slide 4
Kansas Index Well Program
Kansas Geological Survey
Since monitoring began, end-of-season recovery is similar regardless of past pumping or climatic conditions

## Slide 5
KGS Water Balance / Q-Stable Analysis
A simple approach to assess the relationship between average groundwater usage and water-level change
Well suited for Ogallala/High Plains aquifer
  Seasonally pumped
  Water is at depth
  Semi-arid region
Data driven with no conceptualizations
  Water use
  Water levels
Relationships should hold for the next one to three decades

## Slide 6
Wichita County
Kansas Geological Survey
R-squared = 0.81, P < 0.00002
Average 2010-2023:
  Water-level change = -0.35 ft
  Total reported use = 44,066 AF
Average 2019-2023:
  Water-level change = -0.098 ft
  Total reported use = 32,351 AF
Net Inflows = 33,602 AF
Percent reduction for stable water levels:
  Average conditions = 24%
  Drought (2011) = 46%
  Last 5 years = 0%

## Slide 7
Township Scale Groups
Kansas Geological Survey

## Slide 8
10-year water level change and water use density- Wichita County
Kansas Geological Survey
Water-level Change in Feet
Water Use Density (AF/Acre- 2mile circle)

## Slide 9
Wichita County Northeast
Kansas Geological Survey
R-squared = 0.80, P < 0.00002
Average 2010-2023:
  Water-level change = -0.44 ft
  Total reported use = 15,599 AF
Average 2019-2023:
  Water-level change = -0.16 ft
  Total reported use = 11,478 AF
Net Inflows = 11,646 AF
Percent reduction for stable water levels:
  Average conditions = 25%
  Drought (2011) = 49%
  Last 5 years = 0%

## Slide 10
Wichita County Southeast
Kansas Geological Survey
R-squared = 0.51, P < 0.005
Average 2010-2023:
  Water-level change = -0.13 ft
  Total reported use = 4,673 AF
Average 2019-2023:
  Water-level change = 0.016 ft
  Total reported use = 3,270 AF
Net Inflows = 3,605 AF
Percent reduction for stable water levels:
  Average conditions = 23%
  Drought (2011) = 45%
  Last 5 years = 0%

## Slide 11
Wichita County Southwest
Kansas Geological Survey
R-squared = 0.51, P < 0.005
Average 2010-2023:
  Water-level change = -0.11 ft
  Total reported use = 7,114 AF
Average 2019-2023:
  Water-level change = 0.103 ft
  Total reported use = 5,623 AF
Net Inflows = 6,412 AF
Percent reduction for stable water levels:
  Average conditions = 10%
  Drought (2011) = 29%
  Last 5 years = 0%

## Slide 12
Wichita County Northwest
Kansas Geological Survey
R-squared = 0.72, P < 0.0002
Average 2010-2023:
  Water-level change = -0.56 ft
  Total reported use = 16,681 AF
Average 2019-2023:
  Water-level change = -0.34 ft
  Total reported use = 11,981 AF
Net Inflows = 9,987 AF
Percent reduction for stable water levels:
  Average conditions = 40%
  Drought (2011) = 58%
  Last 5 years = 17%

## Slide 13
Wichita County Township 16S 38W
Kansas Geological Survey
R-squared = 0.74, P < 0.00009
Average 2010-2023:
  Water-level change = -0.48 ft
  Total reported use = 6,883 AF
Average 2019-2023:
  Water-level change = -0.06 ft
  Total reported use = 4,963 AF
Net Inflows = 5,073 AF
Percent reduction for stable water levels:
  Average conditions = 26%
  Drought (2011) = 46%
  Last 5 years = 0%

## Slide 14
Wichita County Township 16S 38W, Index Wells
Kansas Geological Survey

## Slide 15
Wichita County
Kansas Geological Survey
On average, 40% decrease in water use for similar climatic conditions.
- about 25% produced by improvement in irrigation efficiency.
- about 15% produced by a decrease in irrigated area (reported decrease 19.9%).

## Slide 16
Wichita County
Kansas Geological Survey
R-squared = 0.81, P < 0.00002
Average 2010-2023:
  Water-level change = -0.35 ft
  Total reported use = 44,066 AF
Average 2019-2023:
  Water-level change = -0.098 ft
  Total reported use = 32,351 AF
Net Inflows = 33,602 AF
Percent reduction for stable water levels:
  Average conditions = 24%
  Drought (2011) = 46%
  Last 5 years = 0%

## Slide 17
Airborne Electromagnetic (AEM) Survey

## Slide 18
How AEM works:
The transmitter fires discrete electromagnetic pulses that generate a primary magnetic field.
The pulses induce eddy currents in the subsurface that generate a secondary magnetic field, i.e. the “response”.
The receiver “listens” for this response – we are measuring this secondary magnetic field.
This measurement provides information on electrical resistivities in the subsurface. Sands and gravels have higher resistivities, while clays, silts, and shale bedrock have lower resistivities.

## Slide 19
GMD4 Flights Lines – 2,443 miles (3,932 km) – May 28-June 16, 2024

## Slide 20
GMD1 Timing – June 2025

## Slide 21: Questions????
Visit our site at http://www.kgs.ku.edu
Kansas Geological Survey
1930 Constant Ave
Lawrence, KS 66047
785-864-2118
Notes: Thank You!